## Slide 1: Why Focus on Conceptual-Stage Optimization?
Reason 1: >80% of the performance of the final design is determined by early-stage design decisions
Example: Transport Aircraft Fuel Burn
Most design opportunities can’t be captured later
Passenger loading: one of many disciplines not typically considered during conceptual design
fuel economy isocontours
existing engines
existing airplanes
common apparent (false) optimum
W/S , …
true optimum
FPR,
Tt 
.
.
.
Pratt’s, GE’s design domain
Boeing’s, Airbus’s design domain
Both figures adapted from Drela, “Simultaneous Optimization of the Airframe, Powerplant, and Operation of Transport Aircraft”. RAeS Conf., 2010
D8.1/8.1b
Mach: 0.72
L/D: 19.5 – 22.0
MTOW: 120 – 130k lb.
Field: 5000 ft.
B737-800
Mach: 0.80
L/D: 15.2
MTOW: 166k lb.
Field: 8000 ft.
Same requirements & tech. assumptions,
fuel burn

## Slide 2: Why Focus on Conceptual-Stage Optimization?
Reason 1: >80% of the performance of the final design is determined by early-stage design decisions
Example: eVTOL Noise
Most design regrets can’t be fixed later
Noise: one of many disciplines not typically considered during conceptual design
Joby Aviation S4
BETA Alia-250
Lilium Jet
On Joby’s conceptual design:
“The very next design principle, behind safety, was noise.”
-Joby Aviation [1]
All images reproduced from their respective manufacturers
Less noise
More noise
[1] SEC 001-39524: “Virtual Fireside with Joby”…
Notes: For low noise, there are certain design choices that you want, from first-principles:
Low tip speed
High solidity
Low disk loading
(ideally) odd number of blades
For example: Beta DOES NOT HAVE THE OPTION of going to a 3-blade configuration, since their concept relies on blade locking in a low-drag configuration for cruise – no amount of blade shape optimization will change that fundamental limit.
https://www.sec.gov/Archives/edgar/data/1819848/000119312521092808/d59889d425.htm
Conceptual Design of the Joby S2 Electric VTOL PAV
https://www.jobyaviation.com/S2ConceptualDesign(AIAA).pdf

## Slide 3: Why Focus on Conceptual-Stage Optimization?
Example: Drones / UAVs
Reason 2: These days, new technologies are enabling more early-stage aircraft design space exploration than ever before
MIT Perdix (Air-launched ALE-55-class ISR UAV)
Black Hornet Nano 18-gram ISR helicopter (Photo: Richard Watt/MOD)
MIT Firefly (Mach 0.8, rocket-propelled micro-UAV)
Transonic DP 545 mph dynamic-soaring glider 100 G sustained turn capability (Photo: Spencer Lisenby)
Able to take more risks with exotic designs:
  Shorter design cycles, lower cost
  Minimal certification and safety risks
New trade spaces to explore
  Packaging/folding – every counts!
  Autonomy & computing SWaP
  Payload miniaturization
  New missions: dull, dirty, and dangerous
    Attritable design and cost optimization
  Physics: scaling laws
    Square-cube
    Reynolds numbers

## Slide 4: Why Focus on Conceptual-Stage Optimization?
Example: Urban Air Mobility / eVTOLs
Reason 2: These days, new technologies are enabling more early-stage aircraft design space exploration than ever before
Figure adapted from SMG Consulting, “AAM Reality Index”
After a decade, still no clear consensus on the “right” way to use electric propulsion.
Electric propulsion is fundamentally different:
 | Conventional | Electric
Energy Storage | Kerosene | Batteries
Energy Transmission | Combustion engines | Electric motors

## Slide 5: Why Focus on Conceptual-Stage Optimization?
Reason 3: The true value of conceptual MDO isn’t only in answering questions (“the point design”) – it’s in determining which questions we should be asking
Requirements Feedback
Which requirements are driving, and which are unimportant?
How should we negotiate requirements?
  Where can we give margin, and where do we need margin?
Market Identification & Competitive Analysis
Given our technologies and capabilities, which customers should we be pitching to?
Where are the market gaps in competitor offerings?
Risk Reduction
How much margin do we have to various constraints?
Which key model assumptions are we sensitive to?
What’s the most cost-effective way to reduce uncertainty in our ability to deliver?